## Slide 1
GROUND IMPROVEMENT TECHNOLOGIES
for a sustainable world
Conclusion
Chart: 
| Case #1 (Dynamic Comcation) | Case #2 (CMC) | Case #3 (SB Wall)
Reduction (t eq. C) | 160 | 1840 | 1855
References
Cortese, A. (2022, December 16). The embodied carbon conundrum: Solving for all emission sources from the built environment. Retrieved January 07, 2023, from https://newbuildings.org/embodied-carbon- conundrum-solving- for-all-emission-sources-from-the-built-environment/
Jones, S., Spaulding, C. and Smyth, P. (2007). " Design and construction of a deep soil-bentonite groundwater barrier wall at Newcastle, Australia " 10th Australian
Leone, M. (2005) – “The Quest for an Environmental Metric.” CFO Publishing Corporation 2007 http://www.cfo.com/printable/article.cfm/5300667
Acknowledgements
Thanks to Charles Spaulding, Frederic Masse, Justin LaBrozzi, the respective authors of the paper.
Chart: 
Alifuzzaman Alif (1904100)
Md. Shahriar Rahman Sakib (1904105)
Mahmudur Rahman (1904116)
Presented By
Tanvir Ahmed Sijan (1904127)
Saif Rahman Sagor (1904122)
For more information scan the QR code
Other
Excavation
ws
Approach
Case #1 Office Building
Pittsburgh, Pennsylvania, USA
Case #2 Luxury Townhouse
Weehawken, New Jersey, USA
Case #3 Steelworks Facility
Australia
Results
Chart: 
| SB | CB
Energy | 209 | 147
Material | 65 | 1982
Labour | 45 | 20
Total | 348 | 2203
Chart: 
| CMC System | H-Pile System
Steel | 0 | 3256
Concrete | 498 | 440.6
Grout | 1358.9 | 0
Total | 1856.9 | 3696
Comparative Emissions for H-Pile and CMC System in t eq. C (Case #2)
Chart: 
| Dynamic Compaction | Initial Design
Fill Material (m³) | 1200 | 12000
Total Diesel (L) | 15000 | 218000
Time Required (Days) | 8 | 30
Comparison between Excavation and Dynamic Compaction (Case #1)
Reduction (t eq. C)
Introduction
In today’s world minimizing the carbon footprints has become a prime concern. Unfortunately, various sectors of construction industry are emitting huge amount of CO2 into the atmosphere. To reduce carbon footprints, a few measures have been taken on ground improvement works. Three ground improvement methods - Dynamic Soil Compaction, Controlled Modulus Column and Soil-Bentonite Wall, are compared with traditional methods for their carbon footprints in light of case histories.
Background
Construction industry alone accounts for 11% of global carbon emissions.
Conventional deep foundation techniques both directly and indirectly contribute to carbon emissions.
Raw material extraction, transportation, construction, operation, maintenance, and demolition all require energy.
Chart: 
| Industry | Transportation | Other | Building materials & Construction | Building Operations
Sales | 30 | 22 | 9 | 11 | 28
Building
Operations
Building Material & Construction
11%
Industry
Transportation
30%
22%
9%
Acceptable geotechnical solutions can directly mitigate unfavorable environmental impacts.
Material selection is one of the the most important factor to determine carbon footprint
Proper technique selection can help achieve long-term sustainability goal with no impact on quality, budget or schedule.
Global Carbon
Emissions
By Sector
Other
Dynamic Compaction
Controlled Modulus Column
Soil Bentonite Wall
A ground improvement technique that densifies soils and fill materials by using a drop weight
Vertical, grouted elements that are used to control and reduce settlement and increase bearing capacity in soft or loose soils.
Typically excavated with a long reach excavator under a bentonite water slurry
Department of Civil Engineering, BUET